## Slide 1: Epileptic seizure recognition using machine learning approaches
Chris Hanson
BME 514
May 05, 2021
See “Notes” for each slide to see additional comments

## Slide 2: Epileptic seizure recognition – Introduction and Background
Original data set:
  500 EEG recordings, each 23.6 seconds long, of individuals either conscious or in a state of seizure.
Modified data set:
  Each of the 500 original EEG recordings has been broken up into 23 data sets, each 1 second long, to increase n. This gives 11500 data sets.
Each EEG has a label (y) indicating whether the individual was actively in seizure during recording.

## Slide 3
I aim to use machine learning algorithms to detect whether an individual is in a state of seizure, based on features extracted from their EEG reading.
Algorithms to be employed:
  K nearest neighbors
  Logistic regression
  Artificial neural network
  Support vector machine
Epileptic seizure recognition – Specific aims

## Slide 4: Epileptic seizure recognition – Methods: The time series
Notes: A glance at some of the datasets suggests that a trend exists, as exemplified above: The normal EEG time series tend to have considerably smaller amplitudes in their fluctuations than do the seizure EEG time series.

## Slide 5
Contribution of periodogram frequency bands (zero padded):
  Delta: 0.5-4 Hz
  Theta: 4-8 Hz
  Alpha: 8-12 Hz
  Beta: 12-35 Hz
  Gamma: 35 - Hz
Median, standard deviation of each time series
Sample entropy
Epileptic seizure recognition – Methods: Feature extraction
Notes: As a follow up to the note in the previous slide, here we see example periodograms of two contrasting time series. While their shape may not differ radically, the scale of the power is notably different, with the seizure time series being orders of magnitude greater.
The relative contribution of each frequency band will be calculated, as a fraction of the total power. The median and standard deviation of the time series will be calculated as well. It is expected that the standard deviation will convey important information that will be critical for the implementation of the machine learning algorithms, as power and variance are related terms – as described in Parseval’s Theorem. Sample entropy will also be calculated.

## Slide 6: Epileptic seizure recognition – Methods: Feature examination
sklearn.feature_selection.SelectKBest
  STD
  Sample entropy
  Gamma
  Beta
  Alpha
  Median
  Theta
  Delta
Notes: SelectKBest is an sklearn package which selects the features which are most predictive of the target, based on univariate statistical tests. The above is the ranked list of the most predictive of the 8 features being used. The graph on the right compares the distribution of the features against each other. Also, the first two principal components are graphed against each other.

## Slide 7: Epileptic seizure recognition – Results: KNN
K scan on test data (K = 4)
  Improved accuracy by ~2%
Distance weighted
  Improved accuracy by ~1%
Manhattan distance used to calculate neighbors
  Improved accuracy by ~1%
Dimensionality reduction via cross validation
  The 1 least correlated dimension was dropped
  Improved accuracy by ~0.5%
Non-scaled features
  Improved accuracy by ~0.2%
Notes: These are the specific alterations I made to the standard KNN algorithm that optimized the predictiveness of the method. They can be seen in my Jupyter notebook.

## Slide 8: Epileptic seizure recognition – Results: KNN
 | Precision | Recall | F1-Score | Support | Accuracy
0 – No seizure | 0.99 | 0.99 | 0.99 | 1869 | 
1 – Seizure | 0.96 | 0.97 | 0.96 | 431 | 
Accuracy |  |  |  |  | 0.99
 | Predicted 0 – No Seizure | Predicted 1 - Seizure
Actual 0 – No seizure | 1853 | 16
Actual 1 - Seizure | 15 | 416
KNN Classification Report:
KNN Confusion Matrix:
KNN 10x cross-validation F1 score:
0.9561064

## Slide 9: Epileptic seizure recognition – Results: KNN Tests
sklearn.feature_selection.SelectKBest
  STD
  Sample entropy
  Gamma
  Beta
  Alpha
  Median
  Theta
  Delta
KNN F-1 with:
  All predictors: 0.956
  Just STD: 0.892
  Just sample entropy: 0.56
  STD & sample entropy: 0.905
  Gamma, beta, alpha, median, theta, delta: 0.830
  2 principal components: 0.884
Notes: Here is a list of 5x cross validation F-1 scores from the KNN algorithm when using a variety of different predictors. This was done mostly to teach me about how robust each method is, and how predictive each feature was.

## Slide 10: Epileptic seizure recognition – Results: Logistic Regression
Scaled features
  Improved accuracy by ~1%
Increased L2 “ridge regularization” parameter
  Improved accuracy by ~0.5%
“Balanced” class weight – under-represented classes given greater weight
  Improved accuracy by ~0.5%
Notes: Graph taken from class notes, as an example of the logistic regression method. Not representative of the data in consideration.
These are the specific alterations I made to the standard logistic regression algorithm that optimized the predictiveness of the method. They can be seen in my Jupyter notebook.

## Slide 11: Epileptic seizure recognition – Results: Logistic Regression
 | Precision | Recall | F1-Score | Support | Accuracy
0 – No seizure | 0.99 | 0.96 | 0.98 | 1869 | 
1 – Seizure | 0.86 | 0.97 | 0.91 | 431 | 
Accuracy |  |  |  |  | 0.96
 | Predicted 0 – No Seizure | Predicted 1 - Seizure
Actual 0 – No seizure | 1800 | 69
Actual 1 - Seizure | 15 | 416
LR Classification Report:
LR Confusion Matrix:
LR 10x cross-validation F1 score:
0.9100394

## Slide 12: Epileptic seizure recognition – Results: Logistic Regression Tests
sklearn.feature_selection.SelectKBest
  STD
  Sample entropy
  Gamma
  Beta
  Alpha
  Median
  Theta
  Delta
Logistic Regression F-1 with:
  All predictors: 0.910
  Just STD: 0.896
  Just sample entropy: 0.544
  STD & sample entropy: 0.897
  Gamma, beta, alpha, median, theta, delta: 0.420
  2 principal components: 0.568
Notes: Here is a list of 5x cross validation F-1 scores from the logistic regression algorithm when using a variety of different predictors. This was done mostly to teach me about how robust each method is, and how predictive each feature was.
**Changes since presentation #3: I had previously stated “Just STD: 0.334, Just sample entropy: 0.00,” but have since found that my code was incorrect when determining this result. This has now been fixed, as seen above.

## Slide 13: Epileptic seizure recognition – Results: ANN
Scaled features
  Improved accuracy by ~1%
Hidden layer size: (4, 3) – 2 hidden layers, 4 & 3 hidden units
  Determined by cross-validation
  Improved accuracy by ~2%
Notes: These are the specific alterations I made to the standard ANN algorithm that optimized the predictiveness of the method. They can be seen in my Jupyter notebook.

## Slide 14: Epileptic seizure recognition – Results: ANN
 | Precision | Recall | F1-Score | Support | Accuracy
0 – No seizure | 0.99 | 0.99 | 0.99 | 1869 | 
1 – Seizure | 0.95 | 0.96 | 0.95 | 431 | 
Accuracy |  |  |  |  | 0.98
 | Predicted 0 – No Seizure | Predicted 1 - Seizure
Actual 0 – No seizure | 1847 | 22
Actual 1 - Seizure | 18 | 413
ANN Classification Report:
ANN Confusion Matrix:
ANN 10x cross-validation F1 score:
0.9537313

## Slide 15: Epileptic seizure recognition – Results: ANN Tests
sklearn.feature_selection.SelectKBest
  STD
  Sample entropy
  Gamma
  Beta
  Alpha
  Median
  Theta
  Delta
ANN F-1 with:
  All predictors: 0.948
  Just STD: 0.815
  Just sample entropy: 0.428
  STD & sample entropy: 0.910
  Gamma, beta, alpha, median, theta, delta: 0.828
  2 principal components: 0.869
Notes: Here is a list of 5x cross validation F-1 scores from the ANN algorithm when using a variety of different predictors. This was done mostly to teach me about how robust each method is, and how predictive each feature was.

## Slide 16: Epileptic seizure recognition – Results: SVM
Scaled features
  Improved accuracy by ~1%
Radial basis kernel (RBF)
  Improved accuracy by ~3%
Increased L2 “ridge regularization” parameter
  Improved accuracy by ~0.5%
Notes: These are the specific alterations I made to the standard SVM algorithm that optimized the predictiveness of the method. They can be seen in my Jupyter notebook.

## Slide 17: Epileptic seizure recognition – Results: SVM
 | Precision | Recall | F1-Score | Support | Accuracy
0 – No seizure | 0.99 | 0.99 | 0.99 | 1869 | 
1 – Seizure | 0.96 | 0.97 | 0.96 | 431 | 
Accuracy |  |  |  |  | 0.99
 | Predicted 0 – No Seizure | Predicted 1 - Seizure
Actual 0 – No seizure | 1853 | 16
Actual 1 - Seizure | 15 | 416
SVM Classification Report:
SVM Confusion Matrix:
SVM 10x cross-validation F1 score:
0.9627562

## Slide 18: Epileptic seizure recognition – Results: SVM Tests
sklearn.feature_selection.SelectKBest
  STD
  Sample entropy
  Gamma
  Beta
  Alpha
  Median
  Theta
  Delta
SVM F-1 with:
  All predictors: 0.962
  Just STD: 0.902
  Just sample entropy: 0.574
  STD & sample entropy: 0.913
  Gamma, beta, alpha, median, theta, delta: 0.773
  2 principal components: 0.887
Notes: These are the specific alterations I made to the standard SVM algorithm that optimized the predictiveness of the method. They can be seen in my Jupyter notebook.

## Slide 19: Epileptic seizure recognition – Results: Final comparison
Discussion and limitations
This shows that many effective machine learning algorithms can be developed to detect seizures based on the chosen features of the EEG, at least for the data set under consideration. Each of SVC, ANN, and KNN appear to be nearly identical, statistically, regarding their ability to correctly predict seizure, while logistic regression is slightly less precise. Each of these methods are significantly improved by the addition of features beyond the one or two most predictive. These algorithms are limited by the fact that they have been trained and tested only on data from one source, which is doubtlessly biased by the methods of data generation and processing that were employed.
Method | 10x X-val F1 mean | 10x X-val F1 STD
KNN | 0.9561 | 0.00591
LR | 0.9100 | 0.00860
ANN | 0.9538 | 0.00804
SVC | 0.9627 | 0.00727
Notes: These are the mean and standard deviation of the 10x cross validation F-1 scores of each machine learning algorithm, after optimizing them for peak performance.
**Sometimes the ANN value comes out much lower, as apparently the algorithm gets stuck in a local minimum for some of the iterations. However more often than not, it is approximately the above value.

## Slide 20: Epileptic seizure recognition – References
“Epileptic Seizure Recognition Data Set,” UCI Machine Learning Repository, Center for Machine Learning and Intelligent Systems
  https://archive.ics.uci.edu/ml/datasets/Epileptic+Seizure+Recognition
Andrzejak RG, Lehnertz K, Rieke C, Mormann F, David P, Elger CE (2001) Indications of nonlinear deterministic and finite dimensional structures in time series of brain electrical activity: Dependence on recording region and brain state, Phys. Rev. E, 64, 061907